WIREWORLD COMPUTER

Binary to BCD converter

2 inputs :
- Data : binary coded LSDB first on 16 bits
- Write : 16 binary pulses of 4 microns. EQ####EQ
10 outputs composed of 5 wire pairs
one pair per 7 segments display

Schematic:
There are several parts :
- Written data latching part which control when the data coming from register 0 will be taken in account
- Reset of 7-segments displayers
- Digit selecter
- Binary adder
- Digit pulse generator
- 2 mega loops

Data latch
There are 3 inputs:
- Data in coming from register 0 ( Bottom left of the picture)
- Write indicating that a new value has been written to register 0 ( Bottom right )
- Set to make load data into the adder of binary 2 BCD converter ( Top right)
There are 2 outputs
- Display reset which will put all 7 segments displays to 0 ( Top left )
- Data out to be loaded into adder ( Top middle )
Internal components
- 1-micron clock loop
- 4-micron clock loop
- 4-micron clock loop with set and reset
- 3 transistors
- 3 xor gates
- 1 loop of 16 4-microns ticks

The set input is filtered by the 1-micron clock and allow to set a loop which generate a 4-micron clock signal. This loop is reset by the input write. Only the first pulse will perform the reset, the following will no more have effect.
The 4-micron periodic signal is splitted to go:
- in the central loop
- to the transistor (2) controlling the signal coming from the 4 micron clock loop. This way is disabled by transistor (1) when the central loop control is full
  The central loop is also splitted to cross over the data signal thanks to the 3 xor gate, then a small feedback loop filter it to let pass only the first bit
The 4-micron loop on the left is controlled by the transistor (2) and control transistor (3) to let data in go to data out.

Normal behaviour consist to have 4-micron loop set and the central loop full. By this way transitor 1 disable signal controlling transistor 2 which let 4-micron loop control transistor 3 and block data in.
Then write signal is set, flushing the 4-micron controlled loop which make central loop empty.Transistor 3 still block data in.
When set signal pass the 1-micron loop clock filter it will set the 4-micron loop which will start to fill the central loop. During the filling of central loop transistor 1 is not actived so signal generated to fill central loop reach transistor 2 and disable the outpout of 4-micron clock. So transistor 3 is not activated and data in can go to data out. Central loop is sized to contain 16 ticks precisely so transitor 3 will let pass only the 16 bits of data in during this stage. After that central loop is full and we go into initial state.

T and not (T xor B) <==> T and B

Carry loop :periode = 193 <=> 32 bits 4-microns
Demultiplexer control loop : period 769 soit 128 bits codes en 4-microns
- 0111 1111 1111 1111 1111 1111 1111 1111 <=> which allow 1 pulse
- 0111 0111 0111 0111 0111 0111 0111 0111 <==> which allow 8 pulses
- 0111 1111 0111 1111 0111 1111 0111 1111 <==> which allow 4 pulses
- 0111 1111 1111 1111 0111 1111 1111 1111 <=> which allow 2 pulses

BCD Adder : period 193 <=> 32 bits 4-microns

Megaloop : period 3841 <=> 640 bits en 4-microns
Megaloop bottom contains (LSDB first):
- 0000 0011 1100 0110 1111 1111 1111 1111 or 0xFFFF63C0
- 0000 0100 0111 0010 0000 0000 0000 0000 or 0x4E20
- 0000 1000 1110 0100 0000 0000 0000 0000 or 0x2710
- 0000 1011 1110 0000 0000 0000 0000 0000 or 0x7D0
- 0000 0101 1111 0000 0000 0000 0000 0000 or 0xFA0
- 0000 1011 1110 0000 0000 0000 0000 0000 or 0x7D0
- 0001 0111 1100 0000 0000 0000 0000 0000 or 0x3E8
- 0001 0011 0000 0000 0000 0000 0000 0000 or 0xC8
- 0000 1001 1000 0000 0000 0000 0000 0000 or 0x190
- 0001 0011 0000 0000 0000 0000 0000 0000 or 0xC8
- 0010 0110 0000 0000 0000 0000 0000 0000 or 0x64
- 0010 1000 0000 0000 0000 0000 0000 0000 or 0x14
- 0001 0100 0000 0000 0000 0000 0000 0000 or 0x28
- 0010 1000 0000 0000 0000 0000 0000 0000 or 0x14
- 0101 0000 0000 0000 0000 0000 0000 0000 or 0xA
- 0100 0000 0000 0000 0000 0000 0000 0000 or 0x2
- 0010 0000 0000 0000 0000 0000 0000 0000 or 0x4
- 0100 0000 0000 0000 0000 0000 0000 0000 or 0x2
- 1000 0000 0000 0000 0000 0000 0000 0000 or 0x1
- 1000 0000 0000 0000 0000 0000 0000 0000 or 0x1

Megaloop top contains (LSDB first):
- 0000 0001 1111 1111 1111 1111 1111 1111 or 0xFFFFFF80
- 0000 0000 0000 0000 0000 0000 0000 0000 or 0x0
- 0000 0000 0000 0000 0000 0000 0000 0000 or 0x0
- 0000 1001 0001 1000 0000 0000 0000 0000 or 0x1890 = 6288
- 0000 0000 0000 0000 0000 0000 0000 0000 or 0x0
- 0000 0000 0000 0000 0000 0000 0000 0000 or 0x0
- 0000 0000 0000 0000 0000 0000 0000 0000 or 0x0
- 0001 0111 1100 0000 0000 0000 0000 0000 or 0x3E8 = 1000
- 0000 0000 0000 0000 0000 0000 0000 0000 or 0x0
- 0000 0000 0000 0000 0000 0000 0000 0000 or 0x0
- 0000 0000 0000 0000 0000 0000 0000 0000 or 0x0
- 0010 0010 0000 0000 0000 0000 0000 0000 0r 0x44 = 68
- 0000 0000 0000 0000 0000 0000 0000 0000 or 0x0
- 0000 0000 0000 0000 0000 0000 0000 0000 or 0x0
- 0000 0000 0000 0000 0000 0000 0000 0000 or 0x0
- 0101 0000 0000 0000 0000 0000 0000 0000 or 0xA = 10
- 0000 0000 0000 0000 0000 0000 0000 0000 or 0x0
- 0000 0000 0000 0000 0000 0000 0000 0000 or 0x0
- 0000 0000 0000 0000 0000 0000 0000 0000 or 0x0
- 1000 0000 0000 0000 0000 0000 0000 0000 or 0x1 = 1

Analyse du convertisseur:
0xFFFFFFFF - 0xFFFF63C0 = 39999 <=> number greater or equal to 40000 will generate a carry
0xFFFF63C0 + 0x4E20 = 0xFFFFB1E0 => 0xFFFFFFFF – 0xFFFFB1E0 = 19999
0xFFFFB1E0 + 0x2710 = 0xFFFFD8F0 => 0xFFFFFFFF – 0xFFFFD8F0 = 9999
0xFFFFD8F0 + 0x7D0 = 0xFFFFE0C0 = > 0xFFFFFFFF – 0xFFFFE0C0 = 7999
0xFFFFE0C0 + 0xFA0 = 0xFFFFF060 => 0xFFFFFFFF – 0xFFFFF060 = 3999
0xFFFFF060 + 0x7D0 = 0xFFFFF830 => 0xFFFFFFFF – 0xFFFFF830 = 1999
0xFFFFF830 + 0x3E8 = 0xFFFFFC18 => 0xFFFFFFFF – 0xFFFFFC18 = 999
0xFFFFFC18 + 0xC8 = 0xFFFFFCE0 => 0xFFFFFFFF – 0xFFFFFCE0 = 799
0xFFFFFCE0 + 0x190 = 0xFFFFFE70 => 0xFFFFFFFF – 0xFFFFFE70 = 399
0xFFFFFE70 + 0xC8 = 0xFFFFFF38 => 0xFFFFFFFF – 0xFFFFFF38 = 199
0xFFFFFF38 + 0x64 = 0xFFFFFF9C => 0xFFFFFFFF – 0xFFFFFF9C = 99
0xFFFFFF9C + 0x14 = 0xFFFFFFB0 => 0xFFFFFFFF – 0xFFFFFFB0 = 79
0xFFFFFFB0 + 0x28 = 0xFFFFFFD8 => 0xFFFFFFFF -0xFFFFFFD8 = 39
0xFFFFFFD8 + 0x14 = 0xFFFFFFEC => 0xFFFFFFFF – 0xFFFFFFEC = 19
0xFFFFFFEC + 0xA = 0xFFFFFFF6 => 0xFFFFFFFF – 0xFFFFFFF6 = 9
0xFFFFFFF6 + 0x2 = 0xFFFFFFF8 => 0xFFFFFFFF – 0xFFFFFFF8 = 7
0xFFFFFFF8 + 0x4 = 0xFFFFFFFC => 0xFFFFFFFF – 0xFFFFFFFC = 3
0xFFFFFFFC + 0x2 = 0xFFFFFFFE => 0xFFFFFFFF – 0xFFFFFFFE = 1
0xFFFFFFFE + 0x1 = 0xFFFFFFFF
0xFFFFFFFF + 0x1 = 0

Registers:
1 : Special register. Return 0 on Read. Content is displayed in decimal
54-55 : Porte A et Non B
56-57-59 :
59-60 : shift
61 : Read 61
62 : Read => R61 + R62
63 : Not